## Slide 1: Weekly Progress
Maurice - Week 6

## Slide 2: To do by this meeting:
Finish Assembly - need to reprint hips/shoulders… UM3 failing, using PRUSA
Continue tweaking reward function + Training = no more Gazebo for now
Start testing motors with raspberry pi - today (need SD card)
Finish Pybullet Model - still need to tweak some things

## Slide 3: 900k steps, some good features noticed

## Slide 4: Behavior in bullet
Arms spread out
Trying to make subtle changes in each timestep (a bit jittery but can be smoothed IRL)
Pitches forward to compensate for battery (small pitch penalty)
Stays on x axis
Faces forward stays upright (yaw, roll)
Does not always use flat part of foot…
Still slides a little bit, not sure if OK

## Slide 5: Things to consider further
My URDF has mass properties based on CURA estimates when 3D printing. May need to weigh actual parts.
Not sure about my friction and damping parameters in terms of accuracy.
Robot still sliding, might be accurate?
Investigate whether jitter comes from double precision when applying the same command as current joint pose or issue in sim.
Timestep = 0.0165sec = 60Hz, same as expected ctrl loop.
How much can I rely on my sensors when porting to the real robot?
Realized my contact callback had errors in bullet, fixed now and re-training.
Try with only velocity based reward fcn to see if trains faster (can train both at once unlike in Gazebo).
I still want to make the Gazebo version work, but it’s on the backburner.

## Slide 6: Some delays with assembly…
Thankfully, Pybullet was easier than expected, so I shifted my plans around and still have time to accomplish my core goal.
Plan to test raspberry pi with controllers today and to finish assembly ASAP (hard deadline by next meeting).
Will keep tweaking/training sim in parallel.

## Slide 7: To do by next meeting:
Finish or nearly finish (90% satisfaction) training
Finish Assembly and basic control structure
Be ready to deploy on Saturday