## Slide 1: Weekly Progress
Maurice - Week 5

## Slide 2: Lots of debugging, reached Gazebo forum limits...
There were many issues with my code, but I finally got everything to work well.. Headless run also works.
Debug possibilities
  Policy actions outside of action space - FIXED
  good for now 200k+ successful timesteps, 35k+ successful episodes (ie resets)
  Reset sometimes iffy, working on this. Seems to have been fixed as far as i can tell
  UNRELATED: Delete/Spawn buggy, not using… Smth to do with waiting for HW Interface
Letting the simulation run for now (headless)
TRY STOP GRAVITY THEN RESET JOINTS!!!!!!!!1

## Slide 3: Learned something! Reward function needs update
6,000 points for this compared to -200 points for untrained policy

## Slide 4: Noticed behavior
Robot knows that the most important thing over time is alive reward, so it jumps into a stable position to maximize this.
Height penalty not as important as alive reward apparently.
Penalties for roll and pitch non-existent since body upright.
No penalty for yaw - mistake on my part, so it can rotate as much as it wants.
Robot tries to stay on x axis to maximize reward over time.
Robot still generating some forward velocity by not staying static.

## Slide 5: Possible fixes
Limit max episode duration (the weird splits thing allows plen to run forever and rack up ‘alive’ rewards for 6000+ total episode reward)
Incr. minimum body height before ‘death’ so this behavior is impossible
Remove points for not facing forward (yaw)
Remove points (more than alive reward) for staying in the same x position or moving to a lower one after each dt - impractical
General update: study human walking to figure out acceptable pitch (+10-15deg) for walking - lower penalty for pitch change
CONSIDERING: Add penalty for rpy velocities? Not sure if practical
Talk to Ian… → Just realized real robot cannot measure joint efforts!!
Ian recommends either ultra specific or ultra simple reward fcn for no exploit
Increase batch size to 512 (currently 100), add hidden layer and change relu

## Slide 6: Tasks for this meeting
Finish Debugging Env/Agent if needed
Figure out Gazebo rendering
Cleanup code (documentation etc) - code even messier now
Modify Agent to save policy in new file for every x# iterations using # as name
Added fcn to save replay buffer (useful data..), consider increasing batch size
Start Training
Physical Assemly - almost there, tweaking some tolerances for hips/shoulders

## Slide 7: To do by next meeting:
Finish Assembly
Clean Code
Continue tweaking reward function
Start testing motors with raspberry pi
Finish (?) Pybullet model (see how far I can get - Ian said he would fork)